## Slide 1: TI II: Computer Architecture Data Representation and Computer Arithmetic
Systems
Representations
Basic Arithmetic
ALU
31
30
0
Sg
Characteristic/ Exponent
Significand/Mantissa/Fraction
23 22
(x + y) + z ≠ x + (y + z)
1 + ε = 1, ε > 0
x + y < x, y > 0

## Slide 2: Content
Introduction
  Single Processor Systems
  Historical overview
  Six-level computer architecture
Data representation and Computer arithmetic
  Data and number representation
  Basic arithmetic
Microarchitecture
  Microprocessor architecture
  Microprogramming
  Pipelining
Instruction Set Architecture
  CISC vs. RISC
  Data types, Addressing, Instructions
  Assembler
Memories
  Hierarchy, Types
  Physical & Virtual Memory
  Segmentation & Paging
  Caches

## Slide 3: Computer Arithmetic
Basics: How to operate on single bits?
  Combinational (or: combinatorial) circuits (pure logic), sequential circuits (includes memory)
  See lectures on Boolean algebra, circuits, semiconductors etc.
Here: computer arithmetic serves as an example for handling larger data units (tables, graphics, …)
Some more formal basics
Methods and circuits for the implementation of the four basic operations +, -, *, /
Operation of an ALU (Arithmetic Logic Unit) of a computer
https://en.wikipedia.org/wiki/Logic_gate
https://en.wikipedia.org/wiki/Flip-flop_(electronics)

## Slide 4: Formal Basics
Humans: typically use the decimal system for calculations (although other systems exist)
Computers: typically use the binary system for calculations
   Thus, a conversion is necessary
Additionally, computer systems use other representations such as octal or hexadecimal for the more compact representation of larger binary numbers
   Therefore, it is important to understand some mathematical foundations of and relations between the different numbering systems
See also math for CS students!
  Here: only a quick overview

## Slide 5: Numbering Systems

## Slide 6: Requirements for Number Systems
It should be able to represent positive and negative numbers of a certain interval [-x : y]
It should be able to represent (roughly) the same amount of positive and negative numbers
The representation should be unambiguous
The representation should make calculations simpler – compare “our” decimal system with
  Roman numerals
  Chinese numerals
  Babylonian numerals
  …
https://en.wikipedia.org/wiki/Numeral_system
Try, e.g., LXIX * XCIX
like you’re used to …

## Slide 7: Number Systems
Most common: positional number systems (https://en.wikipedia.org/wiki/Positional_notation)
Representation of numbers as a sequence of digits zi, with the radix point between z0 and z-1:
  zn zn-1 ... z1 z0 . z-1 z-2 ... z-m e.g. 1234.567
Each position i of the sequence of digits is assigned a value, which is a power bi of the base (or: radix) b of the numbering system
  b-ary numbering system
The value Xb of the number is the sum of all single values of the positions zibi:

## Slide 8: Number Systems
Common number systems in computer science
Hexadecimal system: we typically use the letters A to F to represent the digits with values 10 to 15
Binary system: most important system inside a computer
Octal and Hexadecimal systems: very simple to convert into the binary system, easier to read
fe80::9c0b:605c:16ba:55c2 0x5A3D $47AF3D1E #FFAA33
Base (b) | Number system | Alphabet
2 | Binary system | 0,1
8 | Octal system | 0,1,2,3,4,5,6,7
10 | Decimal system | 0,1,2,3,4,5,6,7,8,9
16 | Hexadecimal system | 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F

## Slide 9: Conversion into b-ary number systems

## Slide 10: Method 1 (following Euclid)
Conversion from the decimal system to a system with base b
Representation of a number
  Z = zn 10n + zn-1 10n-1 + ... + z1 10 + z0 + z-1 10-1 + ... + z-m 10-m
  = yp bp + yp-1 bp-1 + ... + y1 b + y0 + y-1 b-1 + ... + y-q b-q
Generate the digits step-by-step starting with the most significant (leftmost) digit:
  Step 1: search p according to the inequation bp  Z < bp+1
  assign i = p and Zi = Z
  Step 2: derive yi and the remainder Ri by division of Zi by bi yi = Zi div bi Ri = Zi mod bi
  Step 3: Repeat step 2 for i = p-1,… and replace after each step Zi by Ri, until Ri = 0 or until bi is small enough (thus the precision high enough).

## Slide 11: Method 1: example
Conversion of 15741.23310 into the hexadecimal system
Step 1: 163  15741,233 < 164  highest power is 163
 error!
 15741.23310  3D7D.3BA516
Step 2: | 15741.233 | : | 163 | = | 3 | remainder | 3453.233
Step 3: | 3453.233 | : | 162 | = | D | remainder | 125.233
Step 4: | 125.233 | : | 161 | = | 7 | remainder | 13.233
Step 5: | 13.233 | : | 160=1 | = | D | remainder | 0.233
Step 6: | 0.233 | : | 16-1 | = | 3 | remainder | 0.0455
Step 7: | 0.0455 | : | 16-2 | = | B | remainder | 0.00253
Step 8: | 0.00253 | : | 16-3 | = | A | remainder | 0.000088593
Step 9: | 0.000088593 | : | 16-4 | = | 5 | remainder | 0.000012299

## Slide 12: Method 2 (following Horner)
Conversion from the decimal system to a system with base b
Two steps: First consider the integer part of a number, than the decimals
Conversion of the integer part:
If we factor out the integer we get:
Xb = ((...(((zn b + zn-1) b + zn-2) b + zn-3) b ... ) b + z1) b + z0

## Slide 13: Method 2: example (part 1: integer)
Repeated division of the integer part by the base b.
The remainders are the digits of the number Xb from the least to the most significant position.
Conversion of 1574110 into the hexadecimal system
1574110 : 16 = 983 remainder 13 (D16)
98310 : 16 = 61 remainder 7 (716)
6110 : 16 = 3 remainder 13 (D16)
310 : 16 = 0 remainder 3 (316)
 1574110 = 3D7D16

## Slide 14: Method 2: part 2 – conversion of the decimals
We can also write the decimals of a number in the following way:
Yb = ((...((y-m b-1 + y-m+1) b-1 + y-m+2) b-1 + ... +y-2) b-1 + y-1) b-1
Method: We multiply the decimals of the number by base b to get the fractional digits y-i from the most to the least significant position. (But we have to stop if the precision is good enough…)

## Slide 15: Method 2: example (part 2: decimals)
Conversion of 0.23310 into the hexadecimal system:
Stop if precision is good enough
 0.23310  0.3BA516
 error!
0.233 * 16 = 3. 728
0.728 * 16 = 11. 648
0.648 * 16 = 10. 368
0.368 * 16 = 5. 888

## Slide 16: Conversion into the decimal system

## Slide 17: Conversion: Base b  Base 10
We represent the values of the single positions of the number we want to convert in our common decimal system and sum all values.
The value Xb of the number is the sum of all single values of all positions zibi:

## Slide 18: Conversion: Base b  decimal system – Example
Convert 101101.11012 into the decimal system
0.0625
0.25
0.5
45.812510

## Slide 19: Conversion of arbitrary positional number systems
First, convert the number into the decimal system, then use method 1 or 2 to convert into the final system
Special case:
  If the base of one system is a power of the base of another system the conversion is quite simple: Replace a sequence of digits by a single digit or replace a digit by a sequence of digits, respectively.
  - Example: Conversion of 0110100.1101012 into the hexadecimal system
24 = 16  4 binary digits  1 hexadecimal digit
0011 0100 . 1101 0100
hexadezimal 3 4 . D 4
0110100.110101
dual
Fill-in missing zeros to get
complete groups of 4 digits.

## Slide 20: Questions & Tasks
  So, our computer does not even know simple math – what does this tell us?
  Why is the binary system so common in computers?
  Where can you find hex-notations in the context of computer systems?
  How can number conversion introduce errors?

## Slide 21: Negative Numbers

## Slide 22: Representation of negative numbers
We can use four different formats for the representation of negative numbers in computers:
  Absolute value plus sign (V+S)
  Ones’ complement
  Two’s complement
  Offset binary / excess / biased

## Slide 23: Representation with absolute value plus sign (V+S)
One digit represents the sign, typically the MSB
  MSB = Most Significant Bit
The leftmost bit represents the sign of a number (by convention)
  MSB = 0  positive number
  MSB = 1  negative number
Example:
  0001 0010 = +18
  1001 0010 = -18
Disadvantages:
  Separate handling of the signs during addition and subtraction
  There are two representations of the number 0
    One with positive and one with negative sign (+0 and -0)

## Slide 24: Ones’ complement
Flip all single bits of a binary number to get the number with a reversed sign.
This is called a ones’ complement
  n is the number of digits, e.g. n=4  4 bit numbers
Example:
  410 = 01002  -410 = 1011oc
  -410 = (24 –1) – 4 = 1110 = 10112
Again, negative numbers have the MSB = 1
Advantage (compared to absolute value plus sign)
  No separate handling of the MSB during addition or subtraction
Disadvantage
  Still two representations of zero (0000 and 1111 for 4 bit numbers)
zoc = (2n - 1) – z

## Slide 25: Two’s complement
Avoid the disadvantage by adding 1 after applying ones’ complement:
This results in the two’s complement:
Only one representation of the zero!
  0 . . . 0  1 . . . 1oc
   0 . . . 0tc
ztc = 2n - z

## Slide 26: Two’s complement
Disadvantage:
  Asymmetric interval of numbers that can be represented
  The lowest number has a greater absolute value (by 1) than the highest number
Example: 3 bit two’s complement numbers
Again, negative numbers have the MSB = 1
000
001
010
011
100
110
111
101
0
1
2
3
-4
-1
-2
-3

## Slide 27: Representation of negative numbers – examples
Value plus sign: -77 = 1100 11012
Ones‘ complement : -77 = 1011 00102
Two‘s complement : -77 = 1011 00112
Represent –7710 using 8 bits
  7710= 0100 11012
Flip all the bits
Add 1

## Slide 28: Offset binary / excess / biased representation
Commonly used for the representation of exponents of floating point numbers (but also e.g. in signal processing as the converters are unipolar, i.e., they cannot handle negative values).
This representation of an exponent is also called characteristic.
The whole number range is shifted by adding a constant value (offset/excess/bias) so that the smallest number (largest negative value) gets the representation 0…0.
Assuming n digits: Offset = 2n-1
  Example: n=8  Offset 128
The number range is asymmetric.

## Slide 29: Comparison of different representations
000
001
010
011
100
110
111
101
0
1
2
3
-0
-3
-2
-1
Value plus sign
-(2n-1-1) : 2n-1-1
000
001
010
011
100
110
111
101
0
1
2
3
-3
-0
-1
-2
Ones‘ complement
-(2n-1-1) : 2n-1-1
000
001
010
011
100
110
111
101
0
1
2
3
-4
-1
-2
-3
Two‘s complement
-2n-1 : 2n-1-1
000
001
010
011
100
110
111
101
-4
-3
-2
-1
0
3
2
1
Offset
-2n-1 : 2n-1-1

## Slide 30: Overview of the representations
1 1 1
0 1 1
0 1 1
0 1 1
3
1 1 0
0 1 0
0 1 0
0 1 0
2
1 0 1
0 0 1
0 0 1
0 0 1
1
1 0 0
0 0 0
1 1 1, 0 0 0
1 0 0, 0 0 0
0
0 1 1
1 1 1
1 1 0
1 0 1
-1
0 1 0
1 1 0
1 0 1
1 1 0
-2
0 0 1
1 0 1
1 0 0
1 1 1
-3
0 0 0
1 0 0
- - -
- - -
-4
Characteristic
Two‘s complement
Ones‘ complement
Value + Sign
Decimal value
Representation as

## Slide 31: Questions & Tasks
  What do you get if you add 1 to the largest positive number?
  What happens if you subtract 1 from the largest (by absolute value) negative number?
  Thus, what should be done even for simple arithmetic operations like + and – (think of x + y < x, y > 0)?
  Can you represent or in a computer?

## Slide 32: “Real” Numbers (Fixed and floating point)
No, it is not

## Slide 33: Fixed and floating point numbers
Writing numbers on paper we use:
  digits 0 1 2 3 4 5 6 7 8 9
  sign + -
  point .
Representing numbers in a computer we only have:
  Binary digits (i.e. bits) 0 1
  We need rules for representing the value, the sign and the radix point (typically binary point) in a computer
Representing the sign and value: done (see above)
Two ways of representing the point
  Fixed point
  Floating point

## Slide 34: Fixed point numbers
Convention
  The point is (virtually) located at a fixed position within the bit vector representing a binary number.
  Typically, the point follows the LSB (least significant bit).
Characteristic
  Arbitrary numbers can be scaled into this format.
  Negative numbers: use two’s complement.
  Computers typically do not use fixed point numbers internally, but for input and output (e.g. think of amount of money, 37.42€)

## Slide 35: Fixed point numbers
The type "integer" is a special fixed point format.
Some programming languages allow for the definition of integers of different length.
Size (bit) | Typical names | Sign | Number range (using two‘s complement) | 
 |  |  | min | max
8 | char, octet, byte, modern: int8_t or uint8_t | signed | −128 | 127
 |  | unsigned | 0 | 255
16 | Word, Short/short, Integer, modern: int16_t or uint16_t | signed | −32,768 | 32.767
 |  | unsigned | 0 | 65.535
32 | DWord/Double Word, int, long (Windows on 16/32/64 bit systems; Unix/Linux on 16/32 bit systems), modern: int32_t or uint32_t | signed | −2,147,483,648 | 2,147,483,647
 |  | unsigned | 0 | 4,294,967,295
64 | Int64, QWord/Quadword, long long, Long/long (Unix/Linux on 64 bit systems), modern: int64_t or uint64_t | signed | −9,223,372,036,854,775,808 | 9,223,372,036,854,775,807
 |  | unsigned | 0 | 18,446,744,073,709,551,615
128 | Int128, Octaword, Double Quadword | signed | ≈ −1.70141·1038 | ≈ 1.70141·1038
 |  | unsigned | 0 | ≈ 3.40282·1038
Source: Wikipedia

## Slide 36: Floating Point Numbers First: abstract view Be Aware: Computers USE the IEEE-P 754-Floating-Point-Standard

## Slide 37: Floating point representation of numbers
To represent very large or very small numbers we typically use the scientific notation know from school chemistry or physics (so-called log-linear representation):
The base b is fixed for a certain floating point representation (typically 2 or 16) and, thus, is typically not represented explicitly.
Be aware: floating point numbers typically do not use the two’s complement but value plus sign.
The significand is sometimes also called mantissa or fraction, see https://en.wikipedia.org/wiki/Significand. (several different definitions exist…)
X = ± significand · bexponent

## Slide 38: Floating point representation
The position of the radix point of the significand is by convention (e.g. left of the MSB)
The exponent is an integer represented by its characteristic.
The computer uses a fixed number of digits for the significand and the characteristic.
The size of the characteristic determines the number range.
The size of the significand determines the precision of the representation.

## Slide 39: Floating point format
decimal value = (-1)S × (0.significand) × bexponent
exponent = characteristic – b(y – 1) – x
y | y-1 |  | x | x-1 |  | 0
S | characteristic |  |  | significand |  | 

## Slide 40: Normalization
A floating point number is called normalized if the following holds for the mantissa:
Using a binary representation this means that the first digit after the binary point equals 1, i.e., all normalized numbers start with 0.1….
Exception: For the number 0 all digits are zero (0.0…0)

## Slide 41: Normalization
Assuming a special bit pattern for the 0, the first digit of the significand always equals 1.
Therefore, it is not necessary to represent this first digit of the significand internally.
This bit is called the “hidden bit”.
This saves a bit of memory per number or increases the precision using the same number of bits.
Be aware: for all arithmetic operations and during the conversion into other representations this digit must not be neglected!

## Slide 42: Example: representation of 713510
3 different formats with 32 bit each using the base b = 2
Format a: Fixed point using the two’s complement (typical integer)
0 000 0000 0000 0000 0001 1011 1101 11112 = 0000 1BDF16
31
30
0
S

## Slide 43: Example: representation of 713510
Format b: Floating point, normalized:
31
30
0
0 100 0110 1 110 1111 0111 1100 0000 00002 = 46EF 7C0016
S
characteristic
significand
23 22
Format c: Floating point, normalized, first "1" implicit (hidden bit):
31
30
0
0 1000 1101 101 1110 1111 1000 0000 00002 = 46DE F80016
23 22
S
characteristic
remainder of the significand
Notes: Die Hex-Darstellung zeigt die 32 bit der Gleitkommazahl als ganzes.
Bei c) ist der Mantissenteil einfach um 1 bit verschoben.

## Slide 44: Representable number range
The number bit combinations is the same for all three examples (232)
However, the number range and, thus, the density of representable values on the number line is quite different!

## Slide 45: Representable number range
Format a) Numbers between -231 und 231-1
Format b)
negative numbers -(1-2-23) ·2127 ... -0.5·2-128
positive numbers 0.5·2-128 ... (1-2-23)·2127
and ± 0
31
30
0
S
characteristic
significand
23 22
S

## Slide 46: Representable number range
Format c) normalized floating point
negative numbers -(1-2-24)·2127 ... -0.5·2-128
positive numbers 0.5·2-128 ... (1-2-24)·2127
No representation of the 0!
31
30
0
S
characteristic
remainder of the significand
23 22

## Slide 47: Representable number range
a)
b)
c)
underflow
overflow
0
-231
231-1
- (1-2-23)·2127
(1-2-23) ·2127
- 0.5 ·2-128
0.5 ·2-128
- (1-2-24)·2127
(1-2-24) ·2127
- 0.5 ·2-128
0.5 ·2-128
overflow

## Slide 48: Characteristic numbers
In order to compare different floating point formats three characteristic numbers are useful:
  Maxreal: the largest representable, normalized, positive number
  Minreal: the smallest representable, normalized, positive number
  Smallreal: the smallest number that can be added to 1 to get a result larger than 1

## Slide 49: Characteristic numbers – example
Using format b)
maxreal = (1 – 2-23)·2127 minreal = 0.5 · 2-128
If we normalize 1 we get 0.5 · 21 i.e. the significand is 10000000000000000000000.
The closest number larger than 1 representable in this format has in addition to the “1” in bit 22 also a “1” in bit 0.
This results in the significand: 10000000000000000000001
Thus, smallreal = 0.000000000000000000000012· 21 = 2-23· 21 = 2-22
31
30
0
S
characteristic
significand
23 22

## Slide 50: Imprecisions
The gap between two representable floating point numbers grows exponentially with the absolute value of the numbers, while this gap is constant for fixed point numbers.
Therefore, the imprecision when representing large values is higher. There is a trade-off between range and precision.
Computers violate the laws of math valid for real numbers !
  (although some programming languages call this type real)

## Slide 51: Imprecisions
Source: Computer Systems: A Programmer's Perspective

## Slide 52: Example
The associative property (x + y) + z = x + (y + z) does not always hold, even if there is no overflow or underflow.
  Let’s assume: x = 1; y = z = smallreal/2
  (x + y) + z = (1 + smallreal/2) + smallreal/2 = 1 + smallreal/2 = 1
  x + (y + z) = 1 + (smallreal/2 + smallreal/2)
  = 1 + smallreal
   1

## Slide 53: Questions & Tasks
  Which format can represent more different values: 64 bit integer or floating point?
  Why using floating points at all?
  How can you increase the range or precision of floats?
  Why do we normalize floats?
  Why can we live with the imprecisions of floats for many scenarios?
  How can we achieve a higher precision or greater range? At what cost?
  What can we learn from the smallreal example when it comes to the addition of numbers?

## Slide 54: IEEE P 754 Floating Point Standard

## Slide 55: Standardization (IEEE Standard)
IEEE P 754 floating point standard
Many programming languages know floating point numbers with different precision and range
  E.g. using C: float double long double
The IEEE Standard defines several formants for representation, e.g.,
  IEEE single: 32 bit IEEE double: 64 bit IEEE extended: 80 bit

## Slide 56: IEEE P 754 floating point standard
S
characteristic
significand
0
22
23
30
31
8 bit
23 bit
63
11 bit
52 bit
62
52
51
0
S
characteristic
significand
Example formats of the IEEE standard
Be aware that you will also find the term exponent for characteristic
and the terms mantissa or fraction for significand!

## Slide 57: Properties of IEEE P 754
Base b equals 2.
The first bit of the significand is assumed to be “1” (hidden bit), if the characteristic ≠ 0.
Normalization: the hidden bit is left of the binary point, i.e., 1.xxxxx (hidden bit convention)
If the characteristic = 0 it represents the same exponent as if the characteristic = 1.
However, the first bit of the significand is the represented explicitly. The numbers represented this way are called subnormal (denormalized/denormal, https://en.wikipedia.org/wiki/Denormal_number).
This allows the representation of ±0 (significand and characteristic = 0).

## Slide 58: Properties of IEEE P 754
If all bits of the characteristic are “1” this indicates an exception.
  If all bits of the significand are “0” this represents an overflow, i.e. ± . The processor can then trigger error handling.
  If the significand is ≠ 0 this is called NaN (not a number) and is used for signaling, e.g., invalid operations like the square root of a negative number
Internally, processors may use the IEEE standard with 80 bit to minimize rounding errors.

## Slide 59: Some parameters of IEEE P 754
https://en.wikipedia.org/wiki/IEEE_754

## Slide 60: Overview of the 64 bit IEEE format
characteristic | number | remark
0 | (-1)S 0.significand · 2 -1022 | subnormal
1 | (-1)S 1.significand · 2 -1022 | 
… | (-1)S 1.significand · 2 characteristic – 1023 | 
2046 | (-1)S 1.significand · 2 1023 | 
2047 | significand = 0: (-1)S  | overflow
2047 | significand ≠ 0: NaN | not a number

## Slide 61: Literature
IEEE Computer Society:
  IEEE Standard for Binary Floating-Point Arithmetic ANSI/IEEE Standard 754-1985, SIGPLAN Notices, Vol. 22, No. 2, pp 9-25, 1978
D. Goldberg:
  What every computer scientist should know about floating point arithmetic, ACM Computing Surveys, Vol. 13, No. 1, pp. 5-48,1991

## Slide 62: Rounding modes
IEEE requires “correct rounding”:
  The rounded result is as if infinitively precise arithmetic was used to compute the value and then rounded at the end.
  As we will see: three extra bits are enough to achieve this!
IEEE standard defines five rounding modes:
  Round to the nearest number
    Where ties round to the nearest even digit in the required position (“round to even”, the most common rule)
    Where ties round away from zero
  Round to the nearest number toward 0
  Round up to the nearest number toward +
  Round down to the nearest number toward -

## Slide 63: The three “simple” rounding modes
0
Round toward 0
Round toward 0
Round toward +
Round toward -

## Slide 64: Round to even
The most “difficult” rounding mode (but default and the most common):
  Round to the nearest number, where ties round to even
One method: use infinite precise arithmetic, then round
  Requires very long registers, not really efficient
Can this be done with less hardware?
Two situations require rounding when adding or subtracting numbers:
  Carry
  Exponent alignment (remember: add or subtract only if the exponents are equal!)

## Slide 65: Example a: carry during addition – 234 + 851 = 1080
We use base 10 and 3 significant digits in this example!
2.34 ×102
+8.51 ×102
carry -----------
10.85 ×102
rounded to 1.08 ×103

## Slide 66: Example b: different exponents – 234 + 2.56 = 237
(base 10 and 3 significant digits)
2.34 ×102 2.34 ×102
+2.56 ×100 +0.0256 ×102
---------------
2.3656 ×102
rounded to 2.37 ×102
exponent
alignment
required

## Slide 67: Example c: carry and different exponents – 951 + 64.2 = 1020
(base 10 and 3 significant digits)
(alignment and carry) 9.51 ×102 +0.642 ×102
-------------
10.152 ×102
rounded to 1.02 ×103
For each of these examples we have to use “internally” more than 3 significant digits to achieve correct rounding.
There are also situations where more than 3 significant digits are needed even without rounding.

## Slide 68: Example d: subtraction – 147 - 87.6 = 59.4
1.47 ×102
-0.876 ×102
-----------
0.594 ×102
In this example one additional „internal“ digit is sufficient. However, there are cases where this is not sufficient.

## Slide 69: Example e: 101 - 3.76 = 97.2
1.01 ×102 1.01 ×102
-0.0376 ×102 -0.037 ×102
------------- -------------
0.9724 ×102 0.973 ×102
rounded to 0.972 ×102 0.973 ×102
Deleting the least significant digit („6“) from 0.0376 results in 0.973 instead of 0.972.
Thus, here we need more than 3 significant digits for correct rounding!

## Slide 70: Round and guard
If we ignore the “round to even” rule it can be shown that two additional digits are sufficient for correct rounding.
  Guard g - tells us if we have to take a closer look at r. If g=5, then we could be in the middle between two numbers (example: base = 10).
  Round r - if r > 0 then rounding is simple, as we are not in the middle – but what if r = 0? Are we exactly in the middle (i.e. can we apply round-to-even)?
However, "round-to-even“ requires some more effort.

## Slide 71: Example f: 4.5674 + 0.00025001 = 4.5677 (and not 4.5676)
We have 5 significant digits:
4.5674 ×100 4.5674
2.5001 ×10-4 + 0.00025001
-------------
4.56765001
gr
rounded to 4.5677
Round r and guard g are not sufficient – there are some more digits important, but how many?
Idea: Did we drop something while truncating the number to the significant digits?
If yes, then set a sticky-bit

## Slide 72: Sticky bit
For a correct rounding it is sufficient to know, if all digits less significant than the round digit are equal to zero.
A single bit is enough to store this information: "sticky"-bit
If we drop a digit during alignment that was not equal to zero we set the sticky bit (if we have bits, i.e., base = 2, then the sticky bit is simply the OR over all bits less significant than the round bit).
Thus, the sticky bit tells us if we dropped something during alignment (and the necessary truncation due to the limitation of significant digits).
If the result ties, i.e., the distance to the next lower and higher floating point number is the same, then the sticky bit decides if we have to apply round-to-even or we are simply closer to one number.

## Slide 73: Questions & Tasks
  Can IEEE P 754 represent numbers smaller than minreal? What about zero? What is the price to pay?
  Can IEEE P 754 represent numbers larger than maxreal?
  What does “correct rounding” mean – are there no more errors?
  How many digits do we need to get correct results?
  If base = 2, how many extra bits do we need to perform “correct rounding” according to IEEE P 745?
  What is the idea of a sticky-bit?

## Slide 74: Addition And Subtraction

## Slide 75: Addition and subtraction
Circuits for the addition of integers (fixed point, base 2, two’s complement):
  The base of all arithmetic operations
Very simple:
  Subtraction ≙ addition of the negative value
  X - Y = X + (-Y)
We can also describe multiplication and division based on addition (however, more efficient circuits are known)
  For floating point numbers:
    Separate processing of significand/mantissa/fraction and characteristic/exponent
    Again, integer addition forms the base
Thus, basic types of adders are important (https://en.wikipedia.org/wiki/Adder_(electronics))

## Slide 76: From half adder to full adder
Addition of two binary digits a and b results in a sum s and a carry c.
Truth table:
1
0
1
1
0
1
0
1
0
1
1
0
0
0
0
0
c
s
b
a
This is called a half adder

## Slide 77: Half adder
Equations: s = a b  a b = a  b
c = a b
Logic diagram and logic symbol (according to IEC):
=1
CO

a
b
s
c
a
b
s
c
&
1 bit half adder

## Slide 78: Addition of multiple digits
Additional input for the carry of less significant digits necessary.
ai | bi | ci | si | ci+1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
ci is also called carry in CI
ci+1 is also called carry out CO
The truth table describes a full adder

## Slide 79: Equations, logic diagram and symbol
CO

CI
=1
=1
&
 1
&
ci+1
si
bi
ai
ci
Half adder 1
Half adder 2
bi
ai
ci
ci+1
si
Equations:
si = ai  bi  ci
ci+1 = ai ci  bi ci  ai bi = (ai  bi) ci  ai bi
Full adder

## Slide 80: Ripple-carry adder
How to add two integers with n bits?
Simple solution:
  Use a full adder for each bit plus take the carry of the less significant bit as carry in to generate the sum plus the carry out.
  The LSB (least significant bit) needs only a half adder.
CO

CO

CI
CO

CI
CO

CI
s2
c2
a0
b0
c3
cn+1
s1
sn-1
s0
cn
c1
a1
b1
a2
b2
an-1
bn-1

## Slide 81: Problem
The result of a single bit position is valid only if the carry in based on less significant bit positions is computed.
Worst case: the valid values for the carries ripple through all bit positions (thus the name ripple-carry adder).
The time needed to get a stable result is proportional to the bits added.
Therefore, the ripple-carry adder is sometimes also called an asynchronous parallel adder as it takes all bits of the operands in parallel. (asynchronous, because it depends on the value of the operand how long it takes before the output is stable)

## Slide 82: Carry-lookahead adder
In order to avoid the disadvantage of long delays during addition using a carry-ripple adder,
the carry-lookahead adder directly determines all carries based on the input operands
Equations:
  ci+1 = ai bi  (ai  bi) ci = gi  pi ci
  si = (ai  bi)  ci = pi  ci
  Let’s define:
    gi = ai bi (generate carry) and
    pi = (ai  bi) (propagate carry)
We can derive gi und pi directly from the input bits of the two operands a and b.

## Slide 83: Direct computation of the carries based on the inputs
We can recursively solve the computation of ci+1 by using the terms for ci.
ci+1 = gi  pi ci
This results in
c1 = g0  p0 c0
c2 = g1  p1 g0  p1 p0 c0
c3 = g2  p2 g1  p2 p1 g0  p2 p1 p0 c0
etc.
The time for addition is now (almost…) independent of the number of input bits as the computation of all carries can start immediately by “looking ahead” over all input bit positions – thus the name carry-lookahead adder.

## Slide 84: Logic diagram of a 3 bit carry-lookahead addierer
1
&
&
&
1
c
s
3
g
p
a
b
=1
c
s
2
2
2
g
p
2
2
2
a
b
=1
c
s
1
1
1
=1
&
g
p
1
1
1
a
b
=1
0
0
0
0
0
=1
&
=1
&
c
0
0
&
&
&
1
c
parallel
logic for carries
c3 = g2  p2 g1  p2 p1 g0  p2 p1 p0 c0

## Slide 85: Carry-lookahead-Addierer
Problem:
  The number of logic gates increases with the number of input bits.
  This increases the delay of the gates plus requires more space.
Solution:
  Cascading smaller carry-lookahead adders (carry-ripple between the carry-lookahead adders)
  carry-select adder, conditional sum adder, carry skip-adder, … (https://en.wikipedia.org/wiki/Adder_(electronics))

## Slide 86: Carry-lookahead adder

3
2
1
0
3
2
1
0
CI
CO
3
2
1
0
P
Q


3
2
1
0
3
2
1
0
CI
CO
3
2
1
0
P
Q

0
a
b
s
0
3
4
7
a
a
a
b
b
b
s
s
s
s
s
s
s
0
3
4
7
0
1
2
3
4
5
6
7
-
-
-
-
c
Cascading two 4 bit carry-lookahead adders to add 8 bit integers

## Slide 87: Subtraction
Addition and subtraction

## Slide 88: Subtraction
Subtraction by addition of the two’s complement.
Remember: Two’s complement was flipping all bits and then adding 1.
X - Y = X + (Y + 1) = X +Y + 1
Please note:
  We assume that both operands X and Y are in the format two’s complement.
  The result is again in the format two’s complement.

## Slide 89: Subtractor
We can use an adder, take the minuend X as it is, invert the single bits of the subtrahend Y, and set the carry in CI.
1

0
1
2
3
0
1
2
3
C
I
C
O
0
1
2
3
P
Q

1
1
1
1
X
Y
X
-
Y
Subtraction of two numbers in two‘s complement format.

## Slide 90: Exception 1
We can distinguish three different cases for an addition
1) Both summands are positive
  the sign bits of both summands are 0
  the result must be positive
  the result is correct only if its sign bit is 0, otherwise we have an overflow
both carries are equal,
thus the result is correct
the carries are not equal,
thus the result is not correct

## Slide 91: Exception 2
2) Both summands are negative
  the sign bits of both summands are 1
  the result must be negative
  the result is correct only if its sign bit is 1, otherwise we have an (negative) overflow
both carries are equal,
thus the result is correct
the carries are not equal,
thus the result is not correct

## Slide 92: Exception 3
3) Both summands have different signs
  the result is always correct
  the sign depends on the absolute value of the subtrahend or minuend
  we can ignore the carry generated by the MSBs
both carries are equal,
thus the result is correct
both carries are equal,
thus the result is correct

## Slide 93: Overflow detection
It is very simple to detect an overflow during the addition/subtraction of integers in two’s complement:
  correct addition: the carries are equal
  overflow: the carries are not equal
We can generate an overflow bit using an XOR (exclusive or).

## Slide 94: Questions & Tasks
  We could use a half adder for the LSB. However, n-bit carry ripple adders can use a full adder for the LSB as well. What for?
  How does an adder react if an overflow occurs? What about the result? What about a subtractor?

## Slide 95: Floating Point Addition

## Slide 96: Floating point addition
How to add two floating point numbers a1 and a2?
a1 = s1 be1 a2 = s2 be2
Example: a1 = 3.21 102
a2 = 8.43 10-1
  3 significant digits.
Remember: Computation is done with two additional digits (guard und round) plus the sticky bit.
significand | G | R | S

## Slide 97: Floating point addition – step 1
1. Exponent alignment
  We can add floating point numbers only if the exponents are equal
First: If e1 < e2, swap the operands to get: d = e1 - e2 ≥ 0
Second: Shift right the significand s2 by d positions
              If d > 2, set the sticky bit, if any of the dropped digits had a value  0 (in case of binary digits, the sticky bit is the OR over all dropped bits).
Example: d = 2 - (-1) = 3
      3.2100 102
      0.0084 102 set the sticky bit because we dropped the 3 of 8.43

## Slide 98: Floating point addition – steps 2 and 3
2. Add the significands
Example:
3.2100 102 0.0084 102 ------------------ 3.2184 102
3. Normalization
  Normalize the sum by shifting the significand and adjusting the exponent/characteristic.

## Slide 99: Floating point addition – step 4
4. Rounding
Round using one of the rounding modes while taking the digits g, r and the sticky bit into consideration
  most common: binary digits (bits) and round-to-even
Example:
3.2100 102 0.0084 102 ------------------ 3.2184 102
Rounded result: 3.22 102

## Slide 100: Example 1: 32 - 2.25 = 30 using 4 significands, base = 2
1.000 * 25 - 1.001 * 21
“Infinite” internal precision
1.000 0000 * 25
-0.000 1001 * 25 align, keep all the bits
0.111 0111 * 25 precise result (= 29.75)
1.110 1110 * 24 normalized
1.111 * 24 round up (= 30)
Using g(uard), r(ound), s(ticky) bits
plus 4 significands
1.000 000 * 25
-0.000 101 * 25 align, drop bit, set sticky
0.111 011 * 25
1.110 11 * 24 normalized
1.111 * 24 round up (= 30)

## Slide 101: Example 2: 32 - 3.75 = 28 using 4 significands , base = 2
1.000 * 25 - 1.111 * 21
“Infinite” internal precision
1.000 0000 * 25
-0.000 1111 * 25 align, keep all the bits
0.111 0001 * 25 precise result (= 28.25)
1.110 0010 * 24 normalized
1.110 * 24 round down (= 28)
Using g(uard), r(ound), s(ticky) bits
plus 4 significands
1.000 000 * 25
-0.000 111 * 25 align, drop bit, set sticky
0.111 001 * 25
1.110 01 * 24 normalized
1.110 * 24 round down (= 28)

## Slide 102: MIPS R10000 Floating Point Unit
See literature for multiplication and division!

## Slide 103: Arithmetic logic UNIt (ALU)

## Slide 104: Arithmetic logic unit
ALU (arithmetic logic unit):
  Part of the execution unit of a processor
  Performs logic and arithmetic operations
Inputs of an ALU:
  Operands and control signals of the control unit
Outputs of an ALU:
  Results and status signals to the control unit
Quite often ALUs in simple processors can operate on integers only. Floating point operations are off-loaded to an FPU (floating point unit) or emulated in software as a sequence of fixed point operations.

## Slide 105: Diagram of a simple ALU
register X
register Y
multiplexer
ALU1
ALU2
arithmetic logic
combinational circuit
ALU3
shifter
register Z
cout
over-
flow
sign
zero
s7
s6
s5
s4
s3
s2
s1
cin
s1 | s2 | ALU1 | ALU2
0 | 0 | X | Y
0 | 1 | X | 0
1 | 0 | Y | 0
1 | 1 | Y | X
s6 | s7 | Z
0 | 0 | ALU3
0 | 1 | ALU3  2
1 | 0 | ALU3  2
1 | 1 | store Z
s3 | s4 | s5 | ALU3
0 | 0 | 0 | ALU1 + ALU2 +cin
0 | 0 | 1 | ALU1 – ALU2 – Not(cin)
0 | 1 | 0 | ALU2 – ALU1 – Not(cin)
0 | 1 | 1 | ALU1  ALU2
1 | 0 | 0 | ALU1  ALU2
1 | 0 | 1 | Not(ALU1)  ALU2
1 | 1 | 0 | ALU1  ALU2
1 | 1 | 1 | ALU1  ALU2

## Slide 106: Example operations of the ALU
Left shift of the ones’ complement of Y stored in Z:
  Control signals: s1… s7 = 10 111 10
    10 : ALU1 = Y
    111: ALU3 = ALU1  ALU2
    10 : Z = ALU3 × 2
Is X > Y ?
  Check status signal "sign" after the operation Y – X.
  Control signals: s1…s7 = 00 010 00 and cin = 1
    00 : ALU1 = X und ALU2 = Y
    010: ALU3 = ALU2 – ALU1 – not(cin)
    00 : Z = ALU3

## Slide 107: Questions & Tasks
  When do we set the sticky bit?
  Why is it enough to store a single sticky bit instead of a value?
  Does the ALU support loops, if-then-else etc.?

## Slide 108: Overview
Numbering systems
  Positive numbers
  Negative numbers
  Number conversion
  Real numbers (fixed/floating point)
    Real systems use IEEE!
  Rounding of numbers
Simple circuits
  Addition / Subtraction
  See literature for Multiplication / Division
Arithmetic logic unit (ALU)
  Components of a simple ALU