## Slide 1: TI II: Computer Architecture ISA and Assembly
CISC vs. RISC
Data Types
Addressing
Instructions
Assembler

## Slide 2: Where are we now?
Level 5
Level 3
Level 4
Level 1
Level 0
Level 2
Operating system machine level
ISA (Instruction Set Architecture) level
Microarchitecture level
Assembly language level
Problem-oriented language level
Digital logic level
Translation (Compiler)
Translation (Assembler)
Partial interpretation (operating system)
Hardware
Interpretation (microprogram) or direct execution
Java, C#, C++, C, Haskell, Cobol, …
Java Byte Code, MSIL/CIL
Unix, Windows, iOS
x86, PPC, ARM, …
Netburst, ISSE, ASX, <none>, …
Core i7, ARM9, PPC620, …
Javac, VS .NET
JVM, CLR; JIT/Interpreter
JVM, CLR; JIT/Interpreter
microprogram/ none
hardware

## Slide 3: Information
This chapter is mainly for some background information about ISAs, assembler etc.
The assignments plus tutorials teach you how to program with assembler
We skip the operation system part as this is covered in the course operating systems and networks

## Slide 4: The classical SW/HW boundary
What is visible for the user?

## Slide 5: Execution of operations
Interpretation or compilation of instructions from the ISA-layer
  High-level languages translated into instructions from the ISA
  Pure RISC processors can directly execute ISA instructions
    i.e. the hardware (HW) can execute these instructions
  More complex processors use microprogramming, flexibility and compatibility reasons:
    hardware changes leave ISA unchanged
    reprogramming to circumvent hardware problems
    more powerful ISA – simpler compilers

## Slide 6: A selection of the Pentium II integer instructions
Moves |  |  | Transfer of control |  |  | Condition codes | 
MOV DST,SRC | Move SRC to DST |  | JMP ADDR | Jump to ADDR |  | STC | Set carry bit in EFLAGS register
PUSH SRC | Push SRC onto the stack |  | Jxx ADDR | Conditional jumps based on flags |  | CLC | Clear carry bit in EFLAGS register
POP DST | Pop a word from the stack to DST |  | CALL ADDR | Call procedure at ADDR |  | CMC | Complement carry bit in EFLAGS
XCHG DS1,DS2 | Exchange DS1 and DS2 |  | RET | Return from procedure |  | STD | Set direction bit in EFLAGS register
LEA DST,SRC | Load effective addr of SRC into DST |  | IRET | Return from interrupt |  | CLD | Clear direction bit in EFLAGS reg
CMOV DST,SRC | Conditional move |  | LOOPxx | Loop until condition met |  | STI | Set interrupt bit in EFLAGS register
Arithmetic |  |  | INT ADDR | Initiate a software interrupt |  | CLI | Clear interrupt bit in EFLAGS reg
ADD DST,SRC | Add SRC to DST |  | INTO | Interrupt if overflow bit is set |  | PUSHFD | Push EFLAGS register onto stack
SUB DST,SRC | Subtract DST from SRC |  | Boolean |  |  | POPFD | Pop EFLAGS register from stack
MUL SRC | Multiply EAX by SRC (unsigned) |  | AND DST,SRC | Boolean AND SRC into DST |  | LAHF | Load AH from EFLAGS register
IMUL SRC | Multiply EAX by SRC (signed) |  | OR DST,SRC | Boolean OR SRC into DST |  | SAHF | Store AH in EFLAGS register
DIV SRC | Divide EDX:EAX by SRC (unsigned) |  | XOR DST,SRC | Boolean Exclusive OR SRC to DST |  | Miscellaneous | 
IDIV SRC | Divide EDX:EAX by SRC (signed) |  | NOT DST | Replace DST with 1 s complement |  | SWAP DST | Change endianness of DST
ADC DST,SRC | Add SRC to DST, then add carry bit |  | Shift/rotate |  |  | CWQ | Extend EAX to EDX:EAX for division
SBB DST,SRC | Subtract DST & carry from SRC |  | SAL/SAR DST,# | Shift DST left/right # bits |  | CWDE | Extend 16-bit number in AX to EAX
INC DST | Add 1 to DST |  | SHL/SHR DST,# | Logical shift DST left/right # bits |  | ENTER SIZE,LV | Create stack frame with SIZE bytes
DEC DST | Subtract 1 from DST |  | ROL/ROR DST,# | Rotate DST left/right # bits |  | LEAVE | Undo stack frame built by ENTER
NEG DST | Negate DST (subtract it from 0) |  | RCL/RCR DST,# | Rotate DST through carry # bits |  | NOP | No operation
Binary coded decimal |  |  | Test/compare |  |  | HLT | Halt
DAA | Decimal adjust |  | TST SRC1,SRC2 | Boolean AND operands, set flags |  | IN AL,PORT | Input a byte from PORT to AL
DAS | Decimal adjust for subtraction |  | CMP SRC1,SRC2 | Set flags based on SRC1 - SRC2 |  | OUT PORT,AL | Output a byte from AL to PORT
AAA | ASCII adjust for addition |  | Strings |  |  | WAIT | Wait for an interrupt
AAS | ASCII adjust for subtraction |  | LODS | Load string |  | SRC = source | # = shift/rotate count
AAM | ASCII adjust for multiplication |  | STOS | Store string |  | DST = destination | LV = # locals
AAD | ASCII adjust for division |  | MOVS | Move string |  |  | 
 |  |  | CMPS | Compare two strings |  |  | 
 |  |  | SCAS | Scan Strings |  |  | 

## Slide 7: Complex Instruction Set Computer (CISC)

## Slide 8: Complex Instruction Set Computer (CISC)
Enstehungsgründe für umfangreiche Maschinenbefehlssätze
  Geschwindigkeitsunterschied zwischen CPU und Hauptspeicher
  Mikroprogrammierung
  Kompakter Code
  Unterstützung höherer Programmiersprachen
  Aufwärtskompatibilität
  Marktstrategie

## Slide 9: Complex Instruction Set Computer (CISC)
Gründe dafür
  Ausführung komplizierter Befehle ist immer noch schneller als die Ausführung von Programmen gleicher Funktion
  Mikroprogrammierung begünstigt komplizierte Befehle
  Komplizierte Befehle führen zu kürzeren Programmen, also schnelleres Laden
  Umfang des Befehlssatzes wird oft als Werbeargument verwendet
  Unterstützung höherer Programmiersprachen durch komplizierte Befehle (Direkte Abbildung: Sprachkonstrukt  Befehl)
  Unterstützung von Compilern durch entsprechende Befehle
  Unterstützung spezieller Einsatzgebiete
Fazit
  Entwicklung von Hardware, Programmiersprachen und Einsatzgebieten begünstigt „komplizierte“ Befehle

## Slide 10: Complex Instruction Set Computer (CISC)
Gründe dagegen
  Schnellere Hauptspeicher (Argument der 80er, heute wieder problematisch!) und die Verwendung von Cache-Speichern beschleunigen die Programmausführung
  Mikroprogramme wurden immer komplizierter (immer geringere Unterschiede zwischen Programmierung und Mikroprogrammierung!)
  Ersetzung komplexer Maschinenbefehle durch mehrere einfache Maschinenbefehle
  Verlängerte Entwurfszeit
  Sehr komplexe Steuerwerke
  Sehr umfangreiche Mikroprogramme
  Nur relativ kleine Teile des großen Befehlssatzes werden häufig benutzt

## Slide 11: CISC – ursprüngliche Motivation
Systemprogramme in XPL auf IBM/360:
  90% aller ausgeführten Befehle: 10 verschiedene Befehle
  95% aller ausgeführten Befehle: 21 verschiedene Befehle
  99% aller ausgeführten Befehle: 30 verschiedene Befehle
COBOL-Programme auf IBM/370:
  90,28% aller ausgeführten Befehle: 26 verschiedene Befehle
  99,08% aller ausgeführten Befehle: 48 verschiedene Befehle
  Nur 84 verschiedene Befehle wurden überhaupt benutzt

## Slide 12: The 10 most used instructions in SPECint92 for Intel x86
Instruction | Percentage [%]
load | 22
conditional branch | 20
compare | 16
store | 12
add | 8
and | 6
sub | 5
move register-register | 4
call | 1
return | 1
Total | 95

## Slide 13: Grenzen der CISC Architekturen
Befehlsausnutzung (80/20 Regel)
  nur 20% der Befehle werden überwiegend benutzt
  Viele mächtige Befehle
  komplexes Befehlsformat
  Mikroprogrammierung
Kritisches Problem: Anzahl der Zyklen pro Instruktion (CPI)
  bei vielen CISC Architekturen ist CPI >> 2
    Motorola MC68030: CPI = 4-6
    Intel 80386: CPI = 4-5
  ABER: hochoptimiert in Pentium/Itanium – oft CPI ≈ 1

## Slide 14: Reduced Instruction Set Computer (RISC)

## Slide 15: Reduced Instruction Set Computer (RISC)
The instruction set consists of
  a few, absolutely necessary instructions (≤ 128) and
  instruction formats (≤ 4) with a
  fixed instruction length of 32 bit and only some
  addressing modes (≤ 4).
This allows a much simpler implementation of the control unit and saves space on the chip for additional units.
Many general purpose registers, at least 32, are needed.
Memory access is only possible via special load and store instructions.

## Slide 16: Register/register architecture
Memory access is via load and store operations only.
All other instructions work on the CPU registers only, e.g., arithmetic operations load operands from registers and store results in registers only.
This basic principle is called
  register/register architecture or
  load/store architecture and is typical for many (original) RISC computers.

## Slide 17: Additional features of RISC computers
If possible all instructions should be implemented in a way that they finish within a single processor cycle.
Consequence: pure RISC processors do not use micro programming
  RISC processors introduced enhanced pipelining mechanisms (today, many processors use pipelining for the micro instructions, e.g., Pentium 4).
Furthermore, the early RISC processors had a software controlled pipeline (compilers inserted delay NOPs, introduced delayed jumps etc.) instead of special hardware.
Aside
  PC processors like the Pentium 4 (and up) use micro programming, the internal micro architecture (netburst) is rather RISC, the ISA is CISC.

## Slide 18: RISC
Gründe dafür
  Implementierung auf einem Chip
  Kurze Entwurfszeiten
  Hohe Taktraten, Pipelining
  Neue Verwendungsmöglichkeiten für die eingesparte Chipfläche
Gründe dagegen
  Engpass der Speicheranbindung, heute wieder vergleichsweise langsame Speicher
  Chipfläche nicht mehr so kritisch wie früher

## Slide 19: Early RISC processors
IBM 801 project
  Already 1975, Cocke, IBM research, Yorktown Heights
MIPS project
  Started 1981, Hennessy at the University of Stanford
  The first fully functioning chip was finished in 1983 (NMOS VLSI)
  This project was the starting point of the MIPS corporation.
Berkeley RISC project
  Started 1980, Patterson at UC Berkeley
  Origin of the SPARC processor
  Basic principle of overlapping register windows
  The instruction set contained only 31 instructions with a fixed length of 32 bit and only 2 instruction formats
  Only 3 addressing modes

## Slide 20: RISC-Rechner aus heutiger Sicht
… geblieben ist von der RISC-Idee im Wesentlichen
  das Befehlspipelining
  die Load/Store-Architektur
  ein großer Registersatz: z.B.
    32 allgemeine und
    32 Gleitpunkt-Register
  ein einheitliches Befehlsformat von z.B. 32 Bit
  die Verwendung weniger Adressierungsarten
  der Verzicht auf Mikroprogrammierung
Anmerkung: der Kern eines Pentium 4 (und nachfolgende) folgt RISC-Prinzipien (nur eben für Mikrobefehle!)

## Slide 21: Aufbau eines (puristischen) RISC-Prozessors
Datenteil
Programmteil
Anm.: nicht mehr
klassische
von-Neumann
Architektur!

## Slide 22: Unterschiede zwischen RISC- und CISC-Prozessoren
Havard-Architektur
  getrennter Programm- und Datenspeicher, deshalb zwei Adress- und Datenbusse
  paralleles Holen von Operanden und Instruktionen
Vereinfachende Varianten
  zwei getrennte Bussysteme bis zu den Cache-Speichern, jedoch nur ein Arbeitsspeicher (niedrigere Kosten, heute Standard)
  nur ein Bussystem wie bei Standard-Mikroprozessoren

## Slide 23: Unterschiede zwischen RISC- und CISC-Prozessoren
Steuerwerk
  Festverdrahtet
  Das Befehlsregister als Warteschlange (FIFO) realisiert
  Für jede Pipeline-Stufe ist dort ein Register vorhanden
  Die OpCodes jeder Stufe können vom Schaltnetz des Steuerwerks ausgewertet werden
Registersatz
  besteht aus einer großen Anzahl von Registern
  erlaubt gleichzeitige Auswahl von 3 bis 4 Registern
    z.B. 4 Port Registersatz: gleichzeitiges Schreiben (E0, E1) und Lesen (A0, A1) von jeweils 2 Registern

## Slide 24: Unterschiede zwischen RISC- und CISC-Prozessoren
Rechenwerk
  Besitzt eine Load/Store-Architektur. Die Operanden werden über 2 Operandenbusse aus dem Registersatz herbeigeführt, das Ergebnis (noch im selben Taktzyklus) über den Ergebnisbus in den Registersatz geschrieben.
  Normalerweise gibt es keine direkte Verbindung zwischen ALU und Systemdatenbus, Datentransfer läuft über die Register (Load/Store-Architektur).
Ausnahme
  Register-Bypass zur Vermeidung von Pipeline-Hemmnissen (forwarding techniques)

## Slide 25: The future of RISC?
Today
  Again, processors much faster than RAM/interconnection
  Frequent load/stores as bottleneck
  Integration of > 2 billion transistors on a single chip feasible
Thus
  Development of VLIW (Very Large Instruction Word) processors
  HP/Intel Itanium, very short pipeline, compiler does most of the work, powerful ISA, less memory accesses
  Commercial Failure!
The future?
  RISC considered harmful? Not in embedded systems…
  Will legacy stay there forever…
    seems so with Intel 64 and similar…

## Slide 26: Pentium, SPARC, JVM
Examples of ISAs

## Slide 27: Overview: Pentium, SPARC, JVM
The following processors serve as examples for different ISAs
Pentium
  Originates from the classical x86 CISC architectures
  Still CISC to the outside, but many RISC features inside
  Other CISC examples: Athlon, many old processors (VAX, IBM, ...)
UltraSPARC (Ultra Scalable Processor Architecture)
  Originates from the early RISC projects (like the MIPS processor)
  Still RISC, although extended in many ways
  Can be found in, e.g., SUN computers, industry control systems
  Other RISC examples: Alpha, MIPS, Power, PowerPC
JVM (Java Virtual Machine)
  Either seen as virtual processor or real HW (e.g., picoJava)
  Stack machine (operations take place on a stack)
  Heavily biased by Java
  Other virtual machine examples: CLR, P-Code

## Slide 28: Instruction formats
Example: C:= A + B
Zero-address instruction
  stack architectures: push A; push B; ADD; pop C
One-address instruction
  Accumulator implicitly operand and result: load A; ADD B; st C
Two-address instruction
  One operand becomes result: ADD B,A; move A,C
Three-address format
  ADD C,A,B

## Slide 29: Adressierungsarten
Adressierungsarten
  die verschiedenen Möglichkeiten eines Prozessors die Adresse eines Operanden oder eines Sprungziels im Speicher zu berechnen
Früher
  Adresse der Operanden und Sprungziele absolut im Befehl vorgegeben
Nachteile
  absolute Adressen müssen bereits zur Programmierzeit festgelegt werden  Programme sind lageabhängig im Speicher
  Bei Tabellenzugriffen im Speicher muss die Adresse im Befehl geändert werden  keine Festwertspeicher als Programmspeicher möglich

## Slide 30: Adressierungsarten
Abhilfe
  Adresse wird zur Laufzeit berechnet (dynamische Adressberechnung)
Ablauf der Adressberechnung
Adresse im Programm
dynamische Adressberechnung (explizite, durch den Befehl verlangte Adressrechnung)
Effektive, logische Adresse
Speicherverwaltungseinheit (virtuelle Speicherverwaltung)
Physikalische Adresse

## Slide 31: Adressierungsarten - Überblick

## Slide 32: Register-indirekte Adressierung
Beispiel:
  LD R1, (A0) (load)
  (Lade das Register R1 mit dem Inhalt des durch das Adressregister A0 gegebenen Speicherwortes)
Speicher
Befehlsregister
Prozessor
OpCode
+ / -
Index- oder Basisregister, (Stackpointer)
Operand
AReg
Adresse
(Stackpointer)
Registersatz

## Slide 33: Procedures, Traps, Interrupts & Co.

## Slide 34: Procedures, Traps, Interrupts & Co.
Many reasons for non-linear program execution
  Jumps, branches
  Procedure calls, subroutines, method invocation
  Multithreading, parallel processes, co-routines
  Hardware interrupts (processor external reasons)
  Traps, software interrupts (processor internal reasons)
Non linear program execution is the normal case!
  And invalidates standard cache content ...
    Trace caches can help (more later)

## Slide 35: Program execution
Linear, without branches
With branches

## Slide 36: Procedure call (subroutine, method, ...)

## Slide 37: Co-routine call (parallel process, multithreading,...)

## Slide 38: Behandlung von Ausnahme-Situationen
Während des Betriebs eines Mikroprozessorsystems können Ausnahme-Situationen (Exceptions) auftreten
Ursachen
  Fehler im Betriebssystem bei der Ausführung des Anwenderprogramms oder Fehler der Hardware
  Wunsch externer Systemkomponenten, die Aufmerksamkeit des Prozessors zu erhalten
Eine solche Ausnahme-Situation erfordert eine vorübergehende Unterbrechung oder gar den Abbruch des laufenden Programms

## Slide 39: Behandlung von Ausnahme-Situationen
Die Ausnahme-Behandlung erfolgt durch eine Ausnahmeroutine (Interrupt Service Routine)
Die Auswahl und Aktivierung der Ausnahmeroutine wird durch eine Hardware-Komponente im Steuerwerk unterstützt: Unterbrechungs-System (Interrupt System)
Die Ausnahmeroutine hat Ähnlichkeit mit dem Aufbau eines Unterprogramms
Es gibt jedoch wesentliche Unterschiede

## Slide 40: Ausnahmeroutine/Unterprogramm
Aktivierung
  call subroutine bei Unterprogramm
  INT-Befehl oder Hardware-Aktivierung bei Ausnahmebehandlung
Beendigung
  ret-Befehl bei Unterprogrammen (return from subroutine)
  reti-Befehl bei Ausnahmebehandlung (return from interrupt)
Einsprungadresse ins Unterprogramm direkt im Programm, bei Ausnahmebehandlung über Interrupt-Tabelle
Unterprogrammaufruf sichert meist nur PC auf den Stack, Ausnahmebehandlungs-Aufruf meist auch das PSW

## Slide 41: Ausnahmeroutine/Unterprogramm
Unterprogrammaufrufe werden immer durchgeführt, die meisten Ausnahmebehandlungen werden nur aktiviert, falls das Interrupt Enable Bit im PSW gesetzt ist
Ursachen für Ausnahmebehandlungen
  Prozessorexterne Ursachen (asynchrone Ereignisse)
  Prozessorinterne Ursachen (synchrone Ereignisse)

## Slide 42: Prozessorexterne Ursachen
RESET
  Rücksetzen des Mikrorechnersystems, z.B. ausgelöst durch Taste, Schwankungen der Betriebsspannung, Watch-Dog, ...
HALT
  Anhalten des Prozessors, z.B. zur Vermeidung von Zugriffskonflikten auf dem Systembus bei DMA-Zugriffen
ERROR
  Aufruf einer Fehlerbehandlungsroutine, z.B. bei Bus-Fehlern
Interrupt
  Unterbrechungsanforderung von einem peripheren Gerät, z.B. um verfügbare Daten eines Eingabegerätes anzukündigen
  2 Arten: maskierbar/nicht maskierbar (NMI)

## Slide 43: Prozessorinterne Ursachen
Software Interrupts
  durch INT-Befehl im Programm ausgelöste Unterbrechungen
Traps
  Ausnahmesituationen durch prozessorinterne Ereignisse, z.B. Overflow, Divide by Zero, Stack Overflow

## Slide 44: Calculation of the start address of an Interrupt Service Routine (ISR)
ISR
Memory
Interrupt
Vector
Table
Start Address
Base Address
Interrupt
Source
Int. Vector
Number
x 2, 4, …
Scaling
Data Bus
INT
INTA
+
Address Bus
Base Address
Register

## Slide 45: Ablauf einer ISR I
Interrupt-Aktivierung
Beenden des gerade in Ausführung befindlichen Befehls
Feststellen, ob Software-Interrupt oder interner/externer Hardware-Interrupt vorliegt
Feststellen, ob das Interrupt Enable Bit gesetzt ist  Interrupt zugelassen
Falls HW-Interrupt: Quelle des Interrupts finden, INTA-Leitung (Interrupt Acknowledge) aktivieren
PSW und PC auf den Stack sichern
Interrupt Enable Bit rücksetzen (und damit weitere Unterbrechungen verhindern)

## Slide 46: Ablauf einer ISR II
Startadresse der Interrupt-Service-Routine ermitteln und in den PC laden
Interrupt Service Routine ausführen:
  Meist werden zuerst die benutzten Register auf den Stack gesichert
  Interrupt Enable Bit wieder setzen
  Eigentliche Routine
  Am Ende der Interrupt Service Routine: IRET-Befehl
PSW und PC werden wiederhergestellt und mit dem unterbrochenen Programm wird fortgefahren.
Achtung: Ist eine ISR zu groß blockiert der Rechner!

## Slide 47: Interrupt-Vektortabelle
Oft in Festwertspeicher an spezieller Speicheradresse (z.B. ab Adresse 0000:0000 beim 80X86)
Enthält die Startadressen der Behandlungsroutinen
Interrupt-Quelle liefert bei Interrupt eine Interrupt-Vektor-Nummer (IVN), welche den Eintrag in der Interruptvektor-Tabelle charakterisiert

## Slide 48: Beispiel einer Vektortabelle

## Slide 49: Time sequence of multiple interrupts
Computer with 3 I/O devices
Printer, prio 2
Hard disc, prio 4
RS232, prio 5

## Slide 50: Behandlung mehrerer Interrupt-Quellen
Interrupt-Quellen werden durch Interrupt Controller zyklisch abgefragt (Interrupt-Flag im Statusregister des Controllers).
Komponenten mit gesetztem Interrupt-Flag
  Abfrage abbrechen und die entsprechende Interruptroutine abrufen.
Nach (und auch während) der Abarbeitung eines Interrupts können weitere Anforderungen auftreten.
  Zwei Alternativen zur Behandlung

## Slide 51: Polling: 1. Variante
Zyklische Abfrage wird bei der Komponente fortgesetzt, die in der vorgegebenen Reihenfolge der zuletzt bedienten Komponente folgt  Alle Komponenten haben die gleiche Chance, bedient zu werden („faire“ Prozessor-Zuteilung)
8
2
7
3
5
1
4
6
CPU
8
2
7
3
1
4
6
CPU
5
Aktuell bearbeitete Interrupt-Anforderung
Interrupt-Anforderungen während der Bedienung von Komponente 4

## Slide 52: Polling: 2. Variante
Zyklische Abfrage beginnt immer mit der eindeutig festgelegten ersten Komponente  Verschiedenen Komponenten werden verschiedene Prioritäten zugeordnet. Komponenten mit hoher Priorität werden schneller bedient.
8
2
7
3
5
1
4
6
CPU
8
2
7
3
1
4
6
CPU
5
Aktuell bearbeitete Interrupt-Anforderung
Interrupt-Anforderungen während der Bedienung von Komponente 4

## Slide 53: Polling
Prioritäten beim 80286:
Priorität Ausnahmesituation
  0 RESET Rücksetzen, Initialisieren
  1 TRAPS Ausnahme bei Befehlsausführung
  INT Software-Interrupt
  2 TRACE Einzel-Schritt-Ausführung
  3 NMI nicht maskierbare Interrupts
  4 ... Coprozessor-Fehler
  5 IRQ maskierbare Interrupts
Nachteil des Polling-Verfahrens:
  Die Priorisierung und Identifizierung von Interrupts durch die zyklische Abfrage (Software) ist sehr zeitaufwendig.

## Slide 54: Remember - Interrupt

## Slide 55: Daisy-Chain-Verfahren
Priorisierung und Identifizierung von Interrupts wird durch eine Zusatzhardware durchgeführt.
Zusammenschalten von Interrupt-Quellen zu einer Prioritätskette (Interrupt-Daisy-Chain).
Jede Interrupt-Quelle hat eine Priorisierungsschaltung (dezentrale Priorisierung), die mit der des Vorgängers und Nachfolgers mit Signalleitungen verbunden ist.
Erste Quelle der Kette hat die höchste Priorität. Die Priorität der anderen Quellen nimmt mit jedem Glied in der Kette um eine Stufe ab.

## Slide 56: Daisy-Chain-Verfahren
Interrupt-Quelle 0
mP
Statusregister
IRQ0
IACK
IRQ
IACK0
IE0
IP0
VNR0
Interrupt-Quelle 1
IRQ1
IE1
IP1
VNR1
IACK1
IACK2

## Slide 57: Daisy-Chain-Verfahren
Anforderungen der einzelnen Quellen werden durch ODER zusammengeschaltet (wired or) und über den Interrupt-Eingang IRQ (Kreissymbol) zum Prozessor geführt.
Prozessor leitet (bei gesetzten Interrupt-Enable-Flag) einen Interrupt-Zyklus durch das Aktivieren von IACK ein.
IACK wirkt direkt auf die Interrupt-Quellen und auf den IACK-Eingang der ersten Quelle in der Kette.
Eine Quelle, die während IACK = 1 eine Anforderung anmeldet, verhindert die Weitergabe des aktiven Pegels von IACK an die nachfolgenden Kettenglieder.

## Slide 58: Assembler

## Slide 59: Where are we now?
Level 5
Level 3
Level 4
Level 1
Level 0
Level 2
Operating system machine level
ISA (Instruction Set Architecture) level
Microarchitecture level
Assembly language level
Problem-oriented language level
Digital logic level
Translation (Compiler)
Translation (Assembler)
Partial interpretation (operating system)
Hardware
Interpretation (microprogram) or direct execution
Java, C#, C++, C, Haskell, Cobol, …
Java Byte Code, MSIL/CIL
Unix, Windows, iOS
x86, PPC, ARM, …
Netburst, ISSE, ASX, <none>, …
Core i7, ARM, PPC620, …
Javac, VS .NET
JVM, CLR; JIT/Interpreter
JVM, CLR; JIT/Interpreter
microprogram/ none
hardware

## Slide 60: Compiler vs. Assembler
Assembler
  Source: symbolic representation of a machine language (assembly language)
  Destination: numerical representation of the machine language (instructions from ISA)
  Examples: inline assembler in Visual Studio, MASM, ilasm, asm (gcc, Linux), MMIXal, nasm, ...
Compiler
  Source: high-level language (depends on the definition of „high“ ...), e.g., C, Java, C#, Cobol, Modula, C++, ...
  Destination: assembler language or (built-in assembler) numerical representation of the machine language (instructions from ISA)
  Examples: C#-Compiler in Visual Studio, gcc, cc, javac, ...
Assembler language
  Pure assembler language: 1:1 mapping onto ISA instructions
  But additionally: symbolic names, addresses, labels

## Slide 61: Reasons for an assembler level
Full access to HW features
  (almost) all registers are exposed to the assembler language, all flags can be read or set, many „hidden“ features can be used
    E.g., try accessing the Pentium performance counters from within Java
Performance
  Optimized code for special purposes
    Real-time: exact number of CPU cycles can be counted, guaranteed access times to registers, deterministic response times of sub-routines (again: try Java and real-time – and see what a garbage collector does...)
    Low memory footprint: no useless overhead, optimized loops, etc.
But much harder to program in assembler ....
  Thus typically combined with, e.g., C – only performance critical parts of a program will be tuned via assembler

## Slide 62: Examples for assembler: N = I + J
Pentium
FORMULA:
MOV EAX,I ; register EAX = I
ADD EAX,J ; register EAX = I + J
MOV N,EAX ; N = I + J
I DW 3 ; reserve 4 byte initialized to 3
J DW 4 ; reserve 4 byte initialized to 4
N DW 0 ; reserve 4 byte initialized to 0
SPARC
FORMULA:
SETHI %HI(I),%R1 ! R1 = high-order bits of the address of I
LD [%R1+%LO(I)],%R1 ! R1 = I
SETHI %HI(J),%R2 ! R2 = high-order bits of the address of J
LD [%R2+%LO(J)],%R2 ! R2 = J
NOP ! wait for J to arrive from memory
ADD %R1,%R2,%R2 ! R2 = R1 + R2
SETHI %HI(N),%R1 ! R1 = high-order bits of the address of N
ST %R2,[%R1+%LO(N)] ! N = I + J
I: .WORD 3 ! reserve 4 byte initialized to 3
J: .WORD 4 ! reserve 4 byte initialized to 4
N: .WORD 0 ! reserve 4 byte initialized to 0

## Slide 63: Pseudoinstructions
Pseudoinstructions or assembler directives
  Help a lot for assembler programming
  Depend on designer of the assembler, not the ISA
Examples (MASM for Pentium)
  DB allocate storage for one or more (initialized) bytes
  DW allocate storage for one or more (initialized) 32 bit words
  PROC start a procedure
  MACRO start a macro definition
  INCLUDE fetch and include another file
  IF start conditional assembly based on a given expression
  PUBLIC export a name defined in the module

## Slide 64: Macros vs. procedures
Example macro: swap P, Q
SWAP MACRO
MOV EAX,P
MOV EBX,Q
MOV Q,EAX
MOV P,EBX
ENDM
Differences Macro Procedure
  When is the call made? During assembly During execution
  Is the body inserted into the object program every place the call is made? Yes No
  Is a call instruction inserted into the object program and later executed? No Yes
  Must a return instruction be used after the call is done? No Yes
  How many copies of the body appear in the object program? One per macro call 1
Macros are „textually“ inserted into the assembler program each time a call is made, formal parameters are converted into actual parameters (i.e., the above macro can be used for SWAP A,B as well as SWAP X,Y)

## Slide 65: The assembler process
Step-by-step translation does not work
  Forward references: symbols used before being defined ...
Solution: two-pass translator or single-pass plus conversion into intermediate format
  Pass: reading the source
First step
  Check syntax
  Create a symbol table, opcode table, literal table
  Check instruction length (opcode, operands, ...)
Second step
  Generate object code (*.o, *.obj, ...)
  Generate information for linker

## Slide 66: Generation of an executable binary program

## Slide 67: Structure of an Object Module

## Slide 68: Example object modules
Object module A
0
100
200
300
400
BRANCH TO 200
MOVE P TO X
CALL B
0
100
200
300
400
500
600
BRANCH TO 300
MOVE Q TO X
CALL C
Object module B
0
100
200
300
400
500
Object module C
BRANCH TO 200
MOVE R TO X
CALL D
0
100
200
300
MOVE S TO X
BRANCH TO 200
Object module D
Each module has its own
address space starting at 0

## Slide 69: Objects before/after linking and relocation
Before
relocation and
linking
After
relocation and
linking

## Slide 70: Dynamic linking
A procedure segment
The linkage segment
CALL EAR
TH
CALL EAR
TH
CALL FIRE
CALL AIR
CALL
W
A
TER
CALL
W
A
TER
Indirect
addressing
E
A
R
T
H
A
I
R
F
I
R
E
w
A
T
E
R
Indirect word
Name of the
procedure is
stored as a
character
string
T
o earth
Linkage information
f
or the procedure
of AIR
Indirect
addressing
A procedure segment
The linkage segment
CALL EAR
TH
CALL EAR
TH
CALL FIRE
CALL AIR
CALL
W
A
TER
CALL
W
A
TER
Address of earth
E
A
R
T
H
A
I
R
F
I
R
E
W
A
T
E
R
Invalid address
Invalid address
Before EARTH is called
After EARTH has been called and linked
Invalid address
Invalid address
Invalid address
Invalid address
Invalid address

## Slide 71: Shared libraries
DLL (Dynamic Link Library, Windows), shared library (Unix)
  Save a lot of memory as they appear only once
  Many processes „share“ the same code (instructions)

## Slide 72: Summary
Soft-/Hardware boundary
Complex Instruction Set Computer (CISC)
Reduced Instruction Set Computer (RISC)
Examples of ISA
  Pentium
  SPARC
  JVM
Instructions formats
Addressing formats
Types of instructions
Procedures, Traps, Interrupts & Co.
Assembler